## Slide 1: Class 3.1: Project Specifications
Antony Hodgson, PhD, PEng
ahodgson@mech.ubc.ca
https://ah-ubc.appointlet.com/s/chat-mech328
Available: Mon 9:00-10:45, 1:00-2:00; Wed 1:30-2:45

## Slide 2: Agenda
Review of specification process
  Requirements
  Evaluation Criteria
  Value Equation
    Pet Peeves: Analytical Hierarchical Process and Pugh Charts

## Slide 3: Design Process
Identify Needs
Set Requirements
Design in Detail
Generate Concepts
Evaluate Concepts
Choose Concept
Mission Statement
Build Prototypes
Produce, Maintain, Recycle
Notes: Remind students where we are in design process
My thoughts:
  This is the essence of design
  Most creative and most difficult to teach part of design
  Can be improved but some people are naturally better than others
  MBTI: Intuitive-types are more likely to be better concept generators than Sensing-types (innovation, creativity, imagination, future achievement)

## Slide 4: Design Process
Identify Needs
Set Requirements
Design in Detail
Generate Concepts
Evaluate Concepts
Choose Concept
Mission Statement
Build Prototypes
Produce, Maintain, Recycle
Notes: Remind students where we are in design process
My thoughts:
  This is the essence of design
  Most creative and most difficult to teach part of design
  Can be improved but some people are naturally better than others
  MBTI: Intuitive-types are more likely to be better concept generators than Sensing-types (innovation, creativity, imagination, future achievement)

## Slide 5
Lindmark & Nillson 2014

## Slide 6: MECH 223 Redux
Value Proposition
  Identifies in one sentence who benefits from the intended design, and how
Needs
  Identified for/from stakeholders through research, dialogue, observation, testing
Requirements
  Limits clearly defined so that designer knows when something is good enough
Evaluation Criteria
  Top priorities for optimization
Value Equation
  Expresses trade-offs between ECs – defines optimal design
Notes: Value- need to be conscious of what brings most value. Often use dollars (“most important unit on a drawing”)
Needs – understanding the customer’s wants, perceptions and behaviours; engineer has need to make a living, (profit?), safeguard the public and maintain integrity and reputation.
Need Statements – meant to remove artificial barriers such as poor assumptions about restrictions (number of motors used in project 1
Requirements – getting a clear definition of what is good enough limits the amount of work you have to do. Don’t have time to optimize everything –at minimum need something that works acceptably, is delivered on time within budget

## Slide 7: Final Report Requirements
Refer to important findings from internal and external searches and any research that you performed. Back this up with references to appendices containing details. Appendices should be used to show detailed results of searches.
If you performed preliminary tests, explorations, field trials, etc. to gain an understanding of the design challenge, provide a separate appendix for each one of these that clearly outlines the purpose of the activity, what you hoped to determine, a brief outline of the test in enough detail that it can be replicated, what the test showed and any conclusions that were drawn. Report them here along with research such as results of tests performed by others, related products, patent abstracts, review of relevant standards, etc.
Notes: Don’t read in detail – just highlight

## Slide 8: Final Report Requirements
Identify key needs and their order of priority.
Outline (briefly) the needs assessment process and present the evaluation criteria used to select the concept. Reference an appendix which captures your detailed needs assessment work. This appendix should contain weekly copies of the needs and requirements list that show the weekly evolution of the needs and requirements through the project.
Reference an appendix in which you clearly reveal how you determined the criteria for comparison of concepts and, in the appendix, justify how you determined the relative importance of the criteria.

## Slide 9: Value Proposition
Slack Example: “All your tools in one place” (consumer-oriented)
More realistic engineering problem: “A system (for key stakeholder(s)) that (main function and benefit) while (main constraint)”
Class problem example?

## Slide 10: Need Identification
What are you finding? How? Any problems? Need advice?

## Slide 11: Need Statements
Translation of expressed needs into description of device/system characteristics or behaviours
Five guidelines:
  Describes function, not solution (what, not how)
  Specific
  Positive, not negative
  From point of view of device/system (attribute):
    “Device carries rider of up to 250 lbs”
  (Avoid words like “must” or “should”)

## Slide 12
Ulrich 2002

## Slide 13: Requirements
Definition: a design feature with a clearly defined limit of acceptability
Must be testable
Which is not a requirement?
  The vessel is more than 2 m wide
  The vessel is powered by electricity
  The vessel is maneuverable

## Slide 14: Requirements Template
tinyurl.com/MECH328REQ - Take 5 min and try to write the most important functional requirement for your system (use page for your team; ignore EC for now)

## Slide 15: Design Parameters -> Value
EC
Value Eqn
.
.
.
EC
EC
V
Perf
.
.
.
Perf
Perf
DP
P
S
Notes: Design parameters affect performance variables; performance variables affect satisfaction; satisfaction variables are traded off to maximize value

## Slide 16: Evaluation Criteria
Limit (often has
corresponding requirement);
Has value of 0 at limit
Reasonable shape of curve
Specify key points on curve (eg, midpoint)
Justify all of these

## Slide 17: Evaluation Criterion Exercise
If applicable for your requirement, edit the drawing to produce a corresponding evaluation criterion. Be sure to provide justifications in the spreadsheet for key values and curve shape.

## Slide 18: EC -> Value
‘Value equation’ establishes trade-offs between different aspects of a design, guides design direction
V = w1S1 + w2S2
V = S1S2
V = S1w1S2w2

## Slide 19: Comments on AHP
What AHP is good at:
  Translating judgements/opinions into relative weights (WDM)
  Capturing ‘squishy’ characteristics (eg, “charisma”)
  Documenting decisions
Problems with AHP:
  GIGO – can you trust the opinions of those doing the AHP?
    “We did an AHP – here’s our result. Trust us.”
  Significant complexity, time consuming – requires many pairwise comparisons
  Most useful for scoring specific options; much more suspect for comparing ECs
  Linear functions
Best practices
  Present reasoning as clearly as possible (so reader can decide if they agree)
  Evaluate sensitivity!
  Use ECs as input at bottom layer of AHP whenever possible
Strongly consider using a direct formulation of value equation

## Slide 20: Leadership Selection Example
https://en.wikipedia.org/wiki/Analytic_hierarchy_process_–_leader_example

## Slide 21: Pugh Charts
Dressing up judgement calls (lipstick on a pig)
How do I trust you?
  At least explain your decisions
Better: Use Weighted Decision Matrices from AHP
Best: Direct validation of value equation