## Slide 1: MECH 325 Shaft Accessories

## Slide 2: Objectives
By the end of this section, you should be able to:
  Identify shaft accessories (keys, pins, splines, etc.) and select an accessory of suitable size
  Identify shaft coupling components: U-joints, lock-nuts, retaining rings, etc.

## Slide 3: Use of Shaft Shoulders
Shoulders can also increase mounting stiffness for components
Gear
Gear

## Slide 4: Uses of Shaft Accessories
What are the desirable characteristics for:
  A component (e.g. gear or pulley) mounted to a shaft
  A bearing mounted to a shaft
  Two shafts connected together

## Slide 5: Shaft Accessories
Setscrews
Pins
Keys
Retaining Rings
Splines
Couplings

## Slide 6: Set Screws
Cup point: most common; for ductile materials
Oval point: uses groove or keyway for spotting on shaft
Cone point: ductile shaft; when no adjustment is needed
Flat point: hardened steel shafts; for frequent adjustment and low torque
Half-dog point: for relative positioning; need a mating hole in the shaft

## Slide 7: Set Screw Sizing
Holding “power” (force)
  for resisting torque and axial force
  e.g.:
shaft
gear or pulley
hub
Set screw
D
T

## Slide 8: Team Exercise
In your teams, look through the notes and discuss each of the shaft accessories in terms of:
- The intended use(s)
- How the component is fixed
- How the component fails (fractures or stops functioning)
15 minutes to review and then random teams will asked to present to the class.

## Slide 9: Set Screws
Often used in pairs
A flat, a slot, or a hole machined into the shaft will significantly increase torque transmission

## Slide 10: Pins
Clevis pin: for quick detachment
Dowel pin: for precise location
Taper pin: like dowel pins; self locking
Grooved pin: many shapes; flexes to provide self-locking
Spring pin: easy assembly; less critical tolerances than solid pins
Spiral spring pin: similar to spring pins with better shock and fatigue resistance

## Slide 11: Loading on Pins
shaft
gear or pulley
hub
pin
D
T
Double shear
Single shear

## Slide 12: Pin Failure Loads

## Slide 13: Keys
Want key to fail before shaft (“mechanical fuse”)
Generally choose soft, ductile material

## Slide 14: Keys
F ≈
Failure from Shear
Solve for key length, L
w
H

## Slide 15: Keys
Failure from compression
Force distributed over bearing area (L H/2)
Solve for key length, L

## Slide 16: Gib-Head Key
Disadvantage:

## Slide 18: Woodruff Key Use
Easy to install / remove
Analysis similar to square keys

## Slide 19: Woodruff Key Geometry (Ref.)
Same analysis as rectangular keys above – geometry is different

## Slide 20: Woodruff Keys: Areas
Shear Area
Bearing Area
W
C
B/2
ds

## Slide 21: Keyway Stress Concentrations

## Slide 22: Retaining Rings
Seat in grooves on the shaft to prevent axial motion of supported members
  Introduces stress concentration
Internal or external
Shoulder height and axial thrust capacity varies (see table and file on Vista)

## Slide 23: Retaining Ring Example

## Slide 25: Retaining Ring Failure Loads
Retaining Ring Failure
(Ring Shear)
Thrust load, P
Shaft diameter D
groove depth d
Ring width t
Thrust load, P
Groove Failure
(Groove Yield)

## Slide 26: Shaft Collar
Like a “moveable shoulder” on the shaft
Set screw-style
  Size using set screw relationships above
  Shaft material should be softer than set screw
Clamp-style
  Available in one-piece or two-piece
  Holding power based primarily on
  screw size and material
  One piece good for accessible ends
  of shafts
  Two piece has about 10% more holding power
  than similar one piece
  Also available in double-wide for
  extra holding power

## Slide 27: Shaft Collar Axial Capacity
Approximate Axial Load Capacity* for Two-Piece Split Collar** Alloy Socket Head Cap Screw |  | 
Screw Size | Maximum Screw Torque (in-lbs) | Axial Holding Power (lbs)
4-40 | 14 | 235
6-32 | 26 | 355
8-32 | 46 | 546
10-32 | 67 | 785
¼-28 | 196 | 1510
5/16-24 | 416 | 2412
3/8-24 | 718 | 3653
½-20 | 1755 | 6657
* Based on typical conditions - will vary based on material and installation conditions
** Reduce axial holding power by roughly 10% for one-piece split collar

## Slide 28: Shaft Collar Axial Capacity
Approximate Axial Load Capacity* for Two-Piece Split Collar** Alloy Socket Head Cap Screw (Metric) |  | 
Screw Size | Maximum Screw Torque (N-m) | Axial Holding Power (kN)
M3x0.5 | 2.2 | 1.4
M4x0.7 | 5.0 | 2.4
M5x0.8 | 10.2 | 3.9
M6x1 | 17.3 | 5.6
M8x1 | 45.0 | 10.9
M10x1.25 | 87.8 | 17.0
* Based on typical conditions - will vary based on material and installation conditions
** Reduce axial holding power by roughly 10% for one-piece split collar

## Slide 29: Splines
Analogous to a gear or a series of axial keys
Provides greater torque transmission
Axial sliding motion is possible
  Splines are often hardened against wear due to axial motions
Splines also facilitate changes to the angular orientation of a shaft mounted element
Straight sided or involute

## Slide 30: Standard Dimensions

## Slide 31: Spline Torque Capacity
How much torque can a 5-in diameter, 4 tooth spline with a permanent fit transmit?

## Slide 32: Rigid Couplings
Advantages:
Shafts must be well supported by bearings

## Slide 33: Flexible Couplings
Flexible Sleeve
 = 1  = low
Bellows
 =  9  =  ¼“
Flex Disk
 =  1  =  1/16“
Sliding Disk
 = 1/2  = 1/4”
U-Joint
 =  15
Roller Chain
 =  1.5  =  0.01“

## Slide 34: Design Scenario
Motor
V-Belt
Drive
Shaft with
Bearings
Impeller
Mixing Tank
Impeller
Shaft
Bearing
& Seal
Identify the components you would use to assemble the machine shown

## Slide 35: Spline Examples